Power supply

The first thing to check is the power supply. Start out with the gateway unplugged from mains power, thermostat and boiler disconnected, and the IC's removed from their sockets. Now measure the resistance between the two terminals of X3. This should be in the order of kOs. Check for short circuits if it is lower, or broken connections if it is higher.
OK
Now that you have verified that the device will not blow out a circuit breaker, you can connect it to mains power. Be careful not to touch any of the parts that have 220 Volts on them. Check for 5V +/- 1% between pins 5 and 14 of IC1 and pin 15 and 16 of IC2. Also make sure the polarity is correct. You should get a positive voltage if you put the black probe on the pin mentioned first and the red probe on the second one.
4.95 Volt on IC1 PIN5 and PIN14
4.95 Volt on IC2 PIN 15 and PIN16

Opentherm interfaces

Next measure the voltage on X1. This should produce a value somewhere between 18V and 34.5V. Anything higher means a risk of blowing out IC3. The polarity is not important.
23.6 Volt
If the voltage is correct you can measure the current between the two terminals of X1. It should be between 5mA and 9mA. If you don't have a current setting on your multimeter you can hook up a 100O resistor to X1 and measure the voltage on X1. If you remember your high school physics you have probably already figured out that the voltage should be between 0.5V and 0.9V. Change the value of R11 if the current is not within the expected limits. A higher resistor value results in less current.
0.73Volt using 120 Ohm
If you connect pin 3 of the IC1 socket to ground (e.g. pin 5), the current between the two terminals of X1 should be between 17mA and 23mA (1.7V and 2.3V across a 100O resistor). Deviations can be corrected by changing the value of R12. You increase the current by lowering the resistor value. Don't start manipulating R12 until the correct value of R11 has been determined (see above) because R11 influences both the low and high current values while R12 only affects the high current value.
2.35Volt using 120 Ohm
If opto-coupler OK1 was not yet installed, remove the mains power and plug OK1 into its socket. Make sure it is placed the right way around. Now use two pieces of wire to connect X1 to X2 and plug the mains power back in. You should now find a voltage between 15V and 18V on X2 (and X1).
16.96 Volt
If you connect pin 2 of the IC1 socket to VDD (e.g. pin 14), the voltage on X2 should drop to between 5V and 7V.
6.33 Volt
Measure the voltage on pin 18 of the IC1 socket with pin 3 left open and again when it is connected to ground. In the former case the voltage should be below 1.25V (it is actually expected to be 0V). In the latter case the voltage must be above 1.25V (and will probably be close to 5V).
0Volt and 4.40 Volt
When finished, remove the wires between X1 and X2. Do not continue until all of the above checks have passed.

Serial interface

It is now time to plug IC2 into its socket. Temporarily remove the mains power before doing so. Once you have visually verified that the IC is sitting correctly in the socket and is oriented the right way around, you can plug the mains power back in.
IC2 should produce RS232 level voltages of, ideally, +12V and -12V. It doesn't quite achieve this, but you should measure a voltage between 8.5V and 12V on pin 2 of IC2
9.67 Volt
and between -8.5V and -12V on pin 6 of IC2.
-9.64 Volt
Hint: you can easily access ground via terminal 1 of X1. You should also find the negative RS232 level between pin 5 and pin 2 of the RS232 DB9 connector.
9.63 Volt
Remove the mains power again and place IC1 into its socket. Beware that IC1 is oriented the other way around from IC2. Connect the gateway to a serial port on your PC via a straight cable. Start a terminal emulator program on your computer (like hypertherm or minicom) and configure it for the serial port the gateway is connected to at 9600 baud, 8 bits, no parity. You can also use my Opentherm Monitor utility.
When you reapply the mains power to the gateway you should see a message saying "OpenTherm Gateway 4.0". If you see only garbage appearing on the screen, there may be a baud rate mismatch. Make sure you have configured your terminal emulator program correctly. If you see only some of the characters (like "OpenThery 4.0"), your serial cable could be too long.
20:31:53.029189	OpenTherm Gateway 4.0.1
20:31:53.076896	Thermostat disconnected

If you see nothing at all and you have checked your serial connection to the PC, verify that the PIC is really running. You should measure the following voltages on IC1: pin1=1.25V, pin2=0V, pin3=4.5V, pin4=5V, pin8=5V, pin9=5V, pin10=5V, pin11=5V, pin12=5V, pin13=5V, pin17=3.5V
When serial transmission from the gateway to the PC is working, you can also try to send a command to the gateway. If you type and enter "PR=B" (this may not be echoed to your screen) you should get the date and time the firmware was built. For version 4.0 that is supposed to be "23:40 05-06-2014" ("12:31 02-02-2012" for version 2.1).
20:33:33.156353	PR: B=23:51 11-06-2014

Slave interface

With the serial cable still connected to your PC and the terminal emulator program running, connect your Opentherm thermostat to X1. In the terminal emulator you should now see messages like "T80190000" every second. The exact message depends on the thermostat, but it should be a literal "T", followed by eight hexadecimal digits.
20:36:51.830219	T80190000	Read-Data	Boiler water temperature: 0.00
20:36:52.167074	R80190000	Read-Data	Boiler water temperature: 0.00
20:36:53.044030	T80190000	Read-Data	Boiler water temperature: 0.00
20:36:53.202281	R10010A00	Write-Data	Control setpoint: 10.00
20:36:54.193487	R10010A00	Write-Data	Control setpoint: 10.00
20:36:54.248175	T80190000	Read-Data	Boiler water temperature: 0.00
20:36:55.217944	R80380000	Read-Data	DHW setpoint: 0.00
20:36:55.451277	T80190000	Read-Data	Boiler water temperature: 0.00
20:36:56.245207	R00390000	Read-Data	Max CH water setpoint: 0.00
20:36:56.670006	T80190000	Read-Data	Boiler water temperature: 0.00
20:36:57.272558	R00060000	Read-Data	Remote parameter flags: 00000000 00000000
20:36:57.871230	T80190000	Read-Data	Boiler water temperature: 0.00
20:36:58.308669	R00120000	Read-Data	CH water pressure: 0.00
20:36:59.068522	T80190000	Read-Data	Boiler water temperature: 0.00
20:36:59.323346	R00000000	Read-Data	Status: 00000000 00000000
If you see nothing, or things like "Error 01" or "Error 03", the reference voltage may be wrong. You can modify it with the VR=X command, where X is a number between 0 and 9. The normal value is 3, but due to variations in the used components you may have to change it. If you find you need a value less than 2 or more than 5, check that R5 and R6 have the right values.
It is also possible that your thermostat doesn't produce a perfect opentherm signal. Some users have reported that the Remeha Celcia 20 thermostat suffers from this defect. You can make the gateway less sensitive to some forms of this problem with the "IT=1" serial command.
With the thermostat connected, the voltage on X1 should have dropped below 7V, with short bursts upward once a second. During these bursts the voltage jumps to values between 15V and 18V, but you won't be able to register that with a simple multimeter. If you have an oscilloscope you should see pulses of 500µS and 1mS wide.
5.87 Volt
If you can't get anything other than errors, see if you can get your hands on a different brand or type of thermostat, if only for testing. Perhaps the thermostat does not follow the Opentherm specifications closely enough for the gateway to accept.

Master interface

Connect the Opentherm signal from the boiler to X2, polarity does not matter. You should now see alternating TXXXXXXXX and BXXXXXXXX reports. After a while you may start seeing RXXXXXXXX and AXXXXXXXX reports as well.

20:41:37.355564	R801C0000	Read-Data	Return water temperature: 0.00
20:41:37.793084	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:38.381073	R900E6400	Write-Data	Maximum relative modulation level: 100.00
20:41:38.496193	Error 03
20:41:38.996179	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:39.496189	R00060000	Read-Data	Remote parameter flags: 00000000 00000000
20:41:39.794040	Error 03
20:41:40.199304	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:40.568499	R00000000	Read-Data	Status: 00000000 00000000
   - CH enable: disabled (0)
   - DHW enable: disabled (0)
   - Cooling enable: disabled (0)
   - OTC active: not active (0)
   - CH2 enable: disabled (0)
   - Summer/winter mode: winter (0)
   - DHW blocking: unblocked (0)
20:41:40.793085	Error 03
20:41:41.405368	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:41.635847	R80190000	Read-Data	Boiler water temperature: 0.00
20:41:41.914202	Error 03
20:41:42.609643	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:42.731533	R10010A00	Write-Data	Control setpoint: 10.00
20:41:42.828277	Error 03
20:41:43.777524	R10010A00	Write-Data	Control setpoint: 10.00
20:41:43.818000	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:44.807769	R80380000	Read-Data	DHW setpoint: 0.00
20:41:44.918069	Error 03
20:41:45.032355	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:45.905729	R00390000	Read-Data	Max CH water setpoint: 0.00
20:41:46.002100	Error 03
20:41:46.233598	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:47.002028	R00060000	Read-Data	Remote parameter flags: 00000000 00000000
20:41:47.273560	Error 03
20:41:47.444771	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:48.060641	R00120000	Read-Data	CH water pressure: 0.00
20:41:48.393635	Error 03
20:41:48.649573	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:49.132936	R00000000	Read-Data	Status: 00000000 00000000
   - CH enable: disabled (0)
   - DHW enable: disabled (0)
   - Cooling enable: disabled (0)
   - OTC active: not active (0)
   - CH2 enable: disabled (0)
   - Summer/winter mode: winter (0)
   - DHW blocking: unblocked (0)
20:41:49.433758	Error 03
20:41:49.859462	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:50.202101	R80190000	Read-Data	Boiler water temperature: 0.00
20:41:50.558800	Error 03
20:41:51.060510	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:51.278300	R10010A00	Write-Data	Control setpoint: 10.00
20:41:51.381873	Error 03
20:41:52.266678	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:52.370212	R00060000	Read-Data	Remote parameter flags: 00000000 00000000
20:41:52.747129	Error 03
20:41:53.408316	R00060000	Read-Data	Remote parameter flags: 00000000 00000000
20:41:53.480557	Error 03
20:41:54.433689	R00060000	Read-Data	Remote parameter flags: 00000000 00000000
20:41:54.683689	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:54.760852	B40060301	Read-Ack	Remote parameter flags: 00000011 00000001
   - DHW setpoint transfer: enabled (1)
   - max CH setpoint transfer: enabled (1)
   - DHW setpoint: read/write (1)
   - max CH setpoint: read-only (0)
20:41:55.496180	R00110000	Read-Data	Relative modulation level: 0.00
20:41:55.906280	Error 03
20:41:56.531376	R00110000	Read-Data	Relative modulation level: 0.00
20:41:57.093198	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:57.562626	R001B0000	Read-Data	Outside temperature: 0.00
20:41:57.750142	Error 03
20:41:58.304174	T80190000	Read-Data	Boiler water temperature: 0.00
20:41:58.639712	R801C0000	Read-Data	Return water temperature: 0.00
20:41:59.518807	Error 03
20:41:59.684687	R801C0000	Read-Data	Return water temperature: 0.00
20:42:00.682780	R801C0000	Read-Data	Return water temperature: 0.00
20:42:00.709303	BFFFBFFFF	Unk-DataId	Message ID 251: 65535
20:42:01.710465	R801C0000	Read-Data	Return water temperature: 0.00
20:42:01.922127	T80190000	Read-Data	Boiler water temperature: 0.00
20:42:02.048058	B401C4100	Read-Ack	Return water temperature: 65.00
20:42:02.766743	R900E6400	Write-Data	Maximum relative modulation level: 100.00
20:42:02.874246	Error 03
20:42:03.140799	T80190000	Read-Data	Boiler water temperature: 0.00
20:42:03.872128	R00300000	Read-Data	DHW setpoint boundaries: 0 0
20:42:03.984592	Error 03
20:42:04.329902	T80190000	Read-Data	Boiler water temperature: 0.00
20:42:04.950262	R00000000	Read-Data	Status: 00000000 00000000
   - CH enable: disabled (0)
   - DHW enable: disabled (0)
   - Cooling enable: disabled (0)
   - OTC active: not active (0)
   - CH2 enable: disabled (0)
   - Summer/winter mode: winter (0)
        - DHW blocking: unblocked (0)
If you don't see any BXXXXXXXX reports, you can determine whether it is a hardware or firmware problem by switching the gateway to monitor mode using the "GW=0" serial command, or the Monitor button on the Configuration screen of the OpenTherm Monitor program. In monitor mode, the firmware doesn't have to be able to decode the opentherm messages in order to pass them on. So, if things start working in monitor mode, there is a firmware problem. If the thermostat is still unable to communicate with the boiler in this mode, you should focus your debugging efforts on the hardware of the opentherm line drivers. Test #4 of the diagnostic firmware may be of help with that.
0:43:43.218812	Error 03
20:43:43.282360	T80190000	Read-Data	Boiler water temperature: 0.00
20:43:44.089921	R80190000	Read-Data	Boiler water temperature: 0.00
20:43:44.282359	Error 03
20:43:44.368488	Command: GW=0
20:43:44.393849	GW: 0
20:43:44.487150	T80190000	Read-Data	Boiler water temperature: 0.00
20:43:44.545448	B40194200	Read-Ack	Boiler water temperature: 66.00
20:43:45.511807	T10010A00	Write-Data	Control setpoint: 10.00
20:43:45.563613	BD0010A00	Write-Ack	Control setpoint: 10.00
20:43:46.527405	T00000000	Read-Data	Status: 00000000 00000000
   - CH enable: disabled (0)
   - DHW enable: disabled (0)
   - Cooling enable: disabled (0)
   - OTC active: not active (0)
   - CH2 enable: disabled (0)
   - Summer/winter mode: winter (0)
   - DHW blocking: unblocked (0)
20:43:46.682092	BC0000000	Read-Ack	Status: 00000000 00000000
   - Fault indication: no fault (0)
   - CH mode: not active (0)
   - DHW mode: not active (0)
   - Flame status: flame off (0)
   - Cooling status: not active (0)
   - CH2 mode: not active (0)
   - Diagnostic indication: no diagnostics (0)
   - Electricity production: not active (0)
20:43:47.558686	T00030000	Read-Data	Slave configuration: 00000000 0
20:43:47.807757	BC0030102	Read-Ack	Slave configuration: 00000001 2
   - DHW: present (1)
   - Control type: modulating (0)
   - Cooling: not supported (0)
   - DHW: instantaneous (0)
   - Master pump control: allowed (0)
   - CH2: not present (0)
   - Remote water filling: available/unknown (0)
   - Heat/cool mode control: heat (0)
20:43:48.574598	T80190000	Read-Data	Boiler water temperature: 0.00
20:43:48.871208	B40194200	Read-Ack	Boiler water temperature: 66.00
20:43:49.594837	T10010A00	Write-Data	Control setpoint: 10.00
20:43:49.652450	BD0010A00	Write-Ack	Control setpoint: 10.00
20:43:50.622847	T00000000	Read-Data	Status: 00000000 00000000
   - CH enable: disabled (0)
   - DHW enable: disabled (0)
   - Cooling enable: disabled (0)
   - OTC active: not active (0)
   - CH2 enable: disabled (0)
   - Summer/winter mode: winter (0)
   - DHW blocking: unblocked (0)
20:43:51.830349	T00000000	Read-Data	Status: 00000000 00000000
   - CH enable: disabled (0)
   - DHW enable: disabled (0)
   - Cooling enable: disabled (0)
   - OTC active: not active (0)
   - CH2 enable: disabled (0)
   - Summer/winter mode: winter (0)
   - DHW blocking: unblocked (0)
<SNIP>
20:46:01.386797	Error 03
20:46:02.495235	T00390000	Read-Data	Max CH water setpoint: 0.00
20:46:03.709122	Error 03
20:46:03.974409	Command: GW=0
20:46:04.002975	GW: 0
20:46:04.901475	T00390000	Read-Data	Max CH water setpoint: 0.00
20:46:04.963967	BF0390000	Unk-DataId	Max CH water setpoint: 0.00
20:46:06.455288	OpenTherm Gateway 4.0.1
20:46:06.953110	T10010A00	Write-Data	Control setpoint: 10.00
20:46:07.060499	Error 03
20:46:08.155209	T10010A00	Write-Data	Control setpoint: 10.00
20:46:08.256821	Error 03
20:46:09.370160	T10010A00	Write-Data	Control setpoint: 10.00
20:46:09.465861	Error 03
20:46:10.578195	T10010A00	Write-Data	Control setpoint: 10.00
20:46:10.667044	Error 03
20:46:11.776443	T10010A00	Write-Data	Control setpoint: 10.00
20:46:11.886787	Error 03
20:46:12.980595	T10010A00	Write-Data	Control setpoint: 10.00
20:46:13.079268	Error 03
20:46:14.192803	T10010A00	Write-Data	Control setpoint: 10.00
20:46:14.292078	Error 03

En uitendelijk gaat de thermostaat knipperen met een F

Diagnostic Firmware

1. LED Test: OK

2. Bit timing thermostat

499,975,484,487,490,489,980,975,488,489,492,486,489,491,487,489,494,487,487,490,487,491,490,488,495,485,487,490,982,976,490,489,488,491,489,490,982,975,981,977,490,489,490,490,488,492,489,489,489,496,483,491,488,493,486,492,980.
10010A00 Write-Data Control setpoint: 10.00
492,974,488,489,488,489,489,491,489,487,488,490,488,489,490,490,488,491,486,490,489,490,489,490,489,491,486,492,487,497,481,491,488,490,490,490,488,490,490,489,490,489,490,489,490,489,489,492,487,490,490,490,488,495,484,492,494,485,489,491,488,490,490,490,981.
00000000 Read-Data Status: 00000000 00000000
496,482,498,971,490,490,979,980,483,489,488,496,482,490,489,491,487,490,488,491,987,477,495,977,488,490,488,491,488,491,488,490,489,492,979,977,982,976,982,484,495,484,496,483,496,484,496,483,497,979,487,489,489,491,981.
901815F8 Write-Data Room temperature: 21.97
494,482,497,977,484,490,494,484,488,490,488,489,489,490,490,488,490,488,488,490,488,492,979,483,496,977,490,489,981,978,487,491,488,498,481,490,492,487,490,493,485,491,490,489,489,491,487,491,489,490,489,491,491,488,495,489,483,491,496,483,982.
80190000 Read-Data Boiler water temperature: 0.00
495,975,489,488,489,488,986,970,491,487,489,490,488,490,488,490,488,490,490,489,490,489,488,491,487,493,486,490,984,974,491,488,489,491,488,491,981,976,983,977,489,489,488,491,489,490,490,490,490,489,489,491,488,493,486,492,981.
10010A00 Write-Data Control setpoint: 10.00
495,974,491,486,489,489,488,490,490,487,490,489,489,489,489,488,490,489,491,488,489,489,488,492,488,489,490,489,489,489,490,490,488,490,490,490,491,488,487,491,490,489,489,491,492,488,488,493,485,491,488,490,489,491,488,491,491,489,490,489,487,492,487,498,976.
00000000 Read-Data Status: 00000000 00000000
495,974,490,487,489,489,488,492,486,492,486,490,489,489,489,494,485,488,491,490,486,490,982,976,488,492,488,489,982,978,489,489,489,490,488,491,489,492,487,491,489,492,486,490,495,486,487,497,482,492,487,492,489,489,489,491,488,492,488,490,982.
00110000 Read-Data Relative modulation level: 0.00
494,481,496,974,490,488,489,489,488,489,489,489,490,489,488,489,492,486,490,489,496,482,986,480,495,976,488,493,979,977,488,491,489,490,489,495,484,489,496,483,489,490,489,490,489,490,492,488,488,491,488,491,489,490,490,491,488,490,488,491,982.
80190000 Read-Data Boiler water temperature: 0.00
500,970,490,487,489,488,980,977,488,489,489,490,492,486,487,490,489,489,492,487,488,492,487,490,489,490,488,491,980,977,488,491,489,491,487,491,982,977,981,977,489,490,488,492,488,493,486,491,488,496,483,498,481,491,489,490,982.
10010A00 Write-Data Control setpoint: 10.00

3. Bit timing boiler
540,523,541,523,540,1052,1075,1052,547,517,547,516,548,516,548,516,548,516,547,517,1075,1052,557,516,547,517,547,516,552,517,547,516,548,516,547,516,1076,523,540,524,540,523,541,1058,547,517,547,516,548,516,547,517,547,516,547,517,547,516,1064.
D0100F00 Write-Ack Room setpoint: 15.00
539,524,540,523,541,1051,548,516,547,516,548,516,547,517,547,516,548,517,547,516,547,517,1075,523,541,1051,548,516,1075,1057,547,517,1075,523,541,1051,1076,523,540,524,540,1058,548,516,547,516,548,516,547,517,547,516,548,516,547,516,1064.
C0193700 Read-Ack Boiler water temperature: 55.00
540,523,540,524,540,1052,1075,1052,547,516,547,517,547,516,549,516,547,516,547,517,547,516,548,516,547,516,548,516,1076,1056,547,516,548,516,547,516,1076,1051,1076,1052,554,516,547,516,548,516,547,517,547,516,547,517,547,516,547,517,1063.
D0010A00 Write-Ack Control setpoint: 10.00
540,523,541,523,540,1052,547,516,548,516,547,517,547,516,547,517,548,516,547,517,547,516,548,516,547,517,547,516,547,517,547,516,552,517,547,516,547,517,547,516,547,517,547,516,548,516,547,517,554,516,547,517,547,516,548,516,547,516,548,516,547,517,547,516,1064.
C0000000 Read-Ack Status: 00000000 00000000
540,1052,1075,1052,1075,1052,547,516,548,516,547,517,548,516,547,517,547,516,1076,523,541,1051,547,517,547,516,552,517,547,516,548,516,1075,1052,1076,1051,1076,530,540,523,541,523,540,524,540,523,541,523,540,1052,1076,511,540.
501815FD Write-Ack Room temperature: 21.99
540,523,540,524,540,1052,547,516,548,516,547,516,548,516,547,517,548,516,547,517,547,516,1076,523,540,1052,547,517,1075,1057,547,516,1076,523,540,1052,1075,524,540,523,541,1058,548,516,547,516,548,516,547,517,547,516,548,516,547,517,1063.
C0193700 Read-Ack Boiler water temperature: 55.00
540,523,541,523,540,1052,1075,1052,547,516,548,516,547,517,548,516,547,517,547,516,548,516,547,516,548,516,547,517,1075,1057,547,516,548,516,547,516,1076,1052,1075,1052,554,516,547,517,547,516,548,516,547,517,547,516,547,517,547,516,1064.
D0010A00 Write-Ack Control setpoint: 10.00
540,523,541,523,540,1052,547,516,548,516,547,516,548,516,547,517,548,516,547,517,547,516,548,516,547,517,547,516,547,517,547,516,553,516,547,516,548,516,547,516,548,516,547,517,547,516,547,517,554,516,548,516,547,516,548,516,547,517,547,516,548,516,547,517,1063.
C0000000 Read-Ack Status: 00000000 00000000
539,1052,1076,1051,548,516,547,516,548,516,547,516,548,516,548,517,547,516,548,516,1076,1051,547,517,547,516,1086,1056,1076,523,540,524,540,1052,547,516,1076,523,540,1059,547,517,547,516,547,517,547,516,548,516,547,517,547,516,1064.
40117300 Read-Ack Relative modulation level: 115.00
540,523,540,524,540,1052,547,516,547,517,547,516,548,516,547,517,548,516,548,516,547,517,1075,523,541,1051,548,516,1076,1056,548,516,1076,523,540,1052,1075,524,540,523,541,1059,547,516,547,517,547,517,547,516,548,516,547,517,547,516,1064.
C0193700 Read-Ack Boiler water temperature: 55.00
540,523,540,524,540,1051,1076,1052,547,516,547,517,547,516,549,516,547,516,548,516,547,517,547,516,548,516,547,517,1075,1057,547,516,547,517,547,516,1076,1051,1076,1052,554,516,547,517,547,516,548,516,547,517,547,516,548,516,547,517,1063.
D0010A00 Write-Ack Control setpoint: 10.00
540,524,540,523,541,1051,547,517,547,516,548,516,547,517,547,516,548,517,547,516,547,517,547,516,548,516,547,517,547,516,548,516,552,516,548,516,547,517,547,516,548,516,547,516,548,516,547,517,554,516,548,516,547,517,547,516,548,516,547,517,547,516,548,516,1064.
C0000000 Read-Ack Status: 00000000 00000000
540,524,540,523,540,1062,1076,1051,548,516,547,517,547,516,549,516,547,517,547,516,1076,1052,547,516,547,517,547,517,552,516,547,517,547,516,548,516,1076,523,540,523,541,523,540,1059,547,517,547,516,548,516,547,517,547,516,548,516,547,517,1063.
D0100F00 Write-Ack Room setpoint: 15.00

4. Delay Symmetry
Enter test number: 4
OK1A high-to-low: 8us
OK1A low-to-high: 38us
OK1B high-to-low: 10us
OK1B low-to-high: 4us

5. Voltage Levels
Enter test number: 5
Thermostat: 0.72, 0.:0, 1.95
Boiler: 0.00, 4.42
Reference: 1.21

6. Idle Times
Enter test number: 6
B: 20.655
T: 935.791
B: 196.010
T: 757.959
B: 21.754
T: 936.171
B: 212.269
T: 743.198
B: 292.332
T: 666.046
B: 127.185
T: 827.826
B: 21.754
T: 936.215
B: 161.345
T: 794.150
B: 22.070
T: 932.942
B: 78.643
T: 879.290
B: 20.945
T: 936.485
B: 91.211
T: 869.155
B: 22.050
T: 928.043
B: 28.079
T: 930.826
B: 20.947
T: 933.125
B: 42.384
T: 917.970
B: 20.807
T: 933.740
B: 255.412
T: 699.139
B: 21.887
T: 935.649
B: 270.563
T: 685.465
B: 20.800
T: 937.592
B: 183.599
T: 770.460
B: 23.307
T: 934.201
B: 200.119